## Slide 1: Amateur Radio Mesh Networking
Part 1
By Tom Davis – KB7HTA

## Slide 2: What is an AR Mesh Network?
In many ways, it is the same as the Internet
What you can do on the Internet you can do on a private mesh network.
  Websites
  Email Servers
  Search Engines
  Chat Rooms
  IP Cameras
  VoIP Telephones
  Emergency Services

## Slide 3: What It Is Not?
Not for conducting business (Part 97 Rules)
24/7 Access – No grantees!

## Slide 4: Overview of the System?
The AREDN™ https://www.arednmesh.org/ acronym stands for “Amateur Radio Emergency Data Network” and it provides a way for Amateur Radio operators to create high-speed ad hoc Data Networks for use in Emergency and service-oriented communications.
Mission: The primary goal of the AREDN® project is to empower licensed amateur radio operators to quickly and easily deploy high-speed data networks when and where they are needed.

## Slide 5: Overview Continued
The amateur radio community is able to meet these high-bandwidth digital communication requirements by using FCC Part 97 amateur radio frequency bands to send digital data between devices which are linked with each other to form a self-healing, fault-tolerant data network. Some have described this as an amateur radio version of the Internet. Although it is not intended for connecting people to the Internet, an AREDN™ mesh network will provide typical Internet or intranet-type applications to people who need to communicate across a wide area during an emergency or community event.

## Slide 6: Types of Links

## Slide 7: Backbone Links
As the name implies, these links form the backbone or superhighway along which large amounts of data can travel for long distances at relatively high speed. Typically backbone or “backhaul” links are permanent installations on mountain peaks, tall buildings, or high towers. They are usually point-to-point links with large high-gain antenna systems running on reliable power sources. In some cases these links are designed with redundant radios which help ensure path protection. Backbone links can operate over distances between 10 to 30+ miles.

## Slide 8: Backbone Red Mountain

## Slide 9: Backbone - Apex Peak

## Slide 10: Intermediate
Intermediate links bridge the gaps between endpoint nodes. Their primary purpose is to pass network data, but there may be cases where they also serve as mesh access nodes for users. Sometimes these links are call “mid-mile”, “distribution”, or “relay” nodes. They are usually installed on medium-height towers or buildings in order to achieve high signal quality with good line of sight to other intermediate nodes. Depending on conditions, intermediate links may operate over distances between 3 to 10+ miles.

## Slide 11: Intermediate Link

## Slide 12: End Point Links
Endpoint links are used to connect destination nodes to the mesh network. Sometimes these links are call “last mile”, “tactical”, or “terminal” nodes. Usually these nodes serve either as the originator or the final destination for network traffic. Depending on local conditions, endpoint links typically operate over distances of 3 miles or less.

## Slide 13: Radios Supported by AREDN
Ubiquiti
  Rocket M2/3/5
  Nano Station M2/3/5
  Bullet
TP-Link
  CPE-210/510
  CPE-220
  CPE-610
MikroTik
  hAP AC Lite
List: http://downloads.arednmesh.org/firmware/ubnt/html/stable.html

## Slide 14: Ubiquiti Rocket M2

## Slide 15: Ubiquiti NanoStation

## Slide 16: Ubiquiti Bullet

## Slide 17: TP-Link CPE-210

## Slide 18: MikroTik hAP AC Lite

## Slide 19: Antennas
Most radios come with the antenna attached to the radio, usually a sector antennas (90 °, 120°)
Others, like the Ubiquiti Rocket M2/3/5 need an antenna – advantage or disadvantage?
There are omni-directional, dish and sector (90 °, 120 °) antennas

## Slide 20: Omni-Directional Antennas

## Slide 21: Dish Antennas

## Slide 22: Sector Antennas

## Slide 23: Putting It All Together
Mission: The primary goal of the AREDN® project is to empower licensed amateur radio operators to quickly and easily deploy high-speed data networks when and where they are needed.
Design relay nodes, end point nodes and power sources

## Slide 24: Power Source
Link: http://kb7hta.com/projects/

## Slide 25: Relay Node(s)

## Slide 26: End Point Node

## Slide 27: What Now?
Part of the LVMesh Group has formed a team to deploy AREDN equipment for emergencies and public service.
Corporate Challenge Bicycle Race in Jean, NV on April 24, 2019
Nevada Open Road Challenge on May 19, 2019
Future deployment challenges

## Slide 28: Corporate Challenge Bike Race
The team decided to deploy one of the two hilltop relay nodes just East of Jean.
The deployment of an endpoint node with TV (for viewing live race video) at the start/finish line of the race in Jean.
The deployment of two endpoint nodes with cameras along the race course.

## Slide 29: Relay Node Location

## Slide 30: Relay Node Transport Bag

## Slide 31: Relay Node

## Slide 32: Start/Finish Line Location

## Slide 33: Start/Finish Node

## Slide 34: Camera 1 Node Location

## Slide 35: Camera 2 Node Location

## Slide 36: Camera Endpoint Node

## Slide 37: Race Start

## Slide 38: Start/Finish Race Net Control

## Slide 39: Live Race Video

## Slide 40: Node Status Screen

## Slide 42: In House Connections Tonight

## Slide 43: The End
Stay Tuned for Part 2
Presentation for Download at kb7hta.com/lvmesh/