## Slide 1: Amateur Radio Mesh Networking
Part 2
By Tom Davis – KB7HTA

## Slide 2: What is an AR Mesh Network?
In many ways, it is the same as the Internet
What you can do on the Internet you can do on a private mesh network.
  Websites Mesh Node Status
  Servers LVMesh
  Search Engines
  Chat
  IP Cameras
  VoIP Telephones
  Emergency Services - WinLink

## Slide 3: What It Is Not?
Not for conducting business (Part 97 Rules)
24/7 Access – No guarantees!

## Slide 4: Overview of the System?
The AREDN™ acronym stands for “Amateur Radio Emergency Data Network” and it provides a way for Amateur Radio operators to create high-speed ad hoc Data Networks for use in Emergency and service-oriented communications.
Mission: The primary goal of the AREDN® project is to empower licensed amateur radio operators to quickly and easily deploy high-speed data networks when and where they are needed.

## Slide 5: Overview Continued
The amateur radio community is able to meet these high-bandwidth digital communication requirements by using FCC Part 97 amateur radio frequency bands to send digital data between devices which are linked with each other to form a self-healing, fault-tolerant data network. Some have described this as an amateur radio version of the Internet. Although it is not intended for connecting people to the Internet, an AREDN™ mesh network will provide typical Internet or intranet-type applications to people who need to communicate across a wide area during an emergency or community event.

## Slide 6: Types of Links

## Slide 7: Nevada Open Road Challenge NORC
Goal: Provide a high speed data network between Check Point 7 and the Start/Finish Line of the NORC, near Hiko, NV; and in addition provide VoIP telephone communications, and live video of the race at Check Point 7 and Check Point 8.

## Slide 8: Network Planning Tools
Google Maps - NORC Race Course
Google Maps – NORC Check Point 7 Map
Topographical Maps - USGS TopoView
Link Calculator - Ubiquiti Link Calculator
Google Maps - NORC Mesh Network

## Slide 9: NORC Race Course Map

## Slide 10: NORC Check Point 7 Map

## Slide 11: Link Calc CP7 to NN High

## Slide 12: NORC Mesh Network Map

## Slide 13: Equipment Construction

## Slide 14: Power Source
Link: Power Box Project

## Slide 15: Relay Node(s)

## Slide 16: Relay Node Transport Bag

## Slide 17: Race Day

## Slide 18: Finish/Start Line Manned by Tom Davis, KB7HTA

## Slide 19: Lower Fossil Relay Node Manned by Tristan Davis

## Slide 20: Check Point 8 Manned by Steve Forinella, N6SFX

## Slide 21: North Narrows High Relay Node Manned by Thomas Turner, KI6CCW

## Slide 22: North Narrows High Relay Node Manned by Thomas Turner, KI6CCW

## Slide 23: Check Point 7 Manned by Wayne McGartlin, N7HWM

## Slide 24: Camera Endpoint Node

## Slide 25: Live Race Video

## Slide 26: Checkpoint Cameras
By Thomas Turner KI6CCW
Camera Purchased on Ebay
Mounting the Camera
Camera Software
Demonstration

## Slide 27: Link Example
Select a Volunteer from the Audience
Open Ubiquiti Link Calculator
Search for Street Address
Draw Link from Volunteer’s Home to Apex
Analysis of Link
  Is the link possible
  If so select appropriate hardware
  If not what are other link options
Purchase Equipment and Install - AREDN™

## Slide 28: Radios Supported by AREDN
Ubiquiti
  Rocket M2/3/5
  Nano Station M2/3/5
  Bullet
TP-Link
  CPE-210/510
  CPE-220
  CPE-610
MikroTik
  hAP AC Lite
List: http://downloads.arednmesh.org/firmware/ubnt/html/stable.html

## Slide 29: Ubiquiti Rocket M2

## Slide 30: Ubiquiti NanoStation

## Slide 31: Ubiquiti Bullet

## Slide 32: TP-Link CPE-210

## Slide 33: MikroTik hAP AC Lite

## Slide 34: Antennas
Most radios come with the antenna attached to the radio, usually a sector antennas (90 °, 120°)
Others, like the Ubiquiti Rocket M2/3/5 need an antenna – advantage or disadvantage?
There are omni-directional, dish and sector (90 °, 120 °) antennas

## Slide 35: Omni-Directional Antennas

## Slide 36: Dish Antennas

## Slide 37: Sector Antennas

## Slide 38: What Now?
Part of the LVMesh Group has formed a team to deploy AREDN equipment for emergencies and public service.
Deployable Autonomous Mesh Node Project
Nevada Open Road Challenge May 17, 2020
Mesh Network Expansion to Pahrump
Mesh Network Expansion to Beacon Hill and Moapa Valley
Mesh Network Expansion LV to LA

## Slide 39: Deployable Autonomous Mesh Node Project

## Slide 40: DAMN Equipment Design
Power Source 2 x 20 Watt Solar Panels
Solar Battery Regulator Charge Controller
Sealed Lead Acid Battery 12 V @ 26 AH
DC-DC Power Converters 24 V, 5 V, and 3.3 V
Supports 1 - 3 nodes
CPU - Arduino Uno with Ethernet Shield
Watchdog Timer
Voltage, Current and Atmospheric Sensors
Baofeng 888 - Telemetry Xmit & DTMF Receive
More Information at DAMN Project

## Slide 41: The End
Download Power Point Presentation
Stay Tuned for Part 3